## Slide 1: Development of algorithms for generating connected midsurfaces using feature information in thin-walled parts
PhD Defense Presentation
by
Yogesh H. Kulkarni
Guided by Dr. Anil Sahasrabudhe (Guide) and Dr. Mukund Kale (Co-guide)
21 January 2017

## Slide 2: Agenda
Introduction
Literature Survey
Proposed System
Model Defeaturing
Feature Generalization
Midcurve-Midsurface Computation
Topological Validation
Case Studies
Conclusions

## Slide 3: Introduction

## Slide 4: Introduction
Necessity of Time-to-market
Quicker validation
Modern - Digital Product Development
CAD-CAE Workflow
Components of Model Simplification
Dimension Reduction: Midsurface, Bar

## Slide 5: Midsurface Advantages
Thin-walled : Sheet Metal, Plastics
Expensive Solid Mesh elements
Advantages of Shell elements
Comparison of results
Lesser computations/time.

## Slide 6: Motivation for Research in Midsurface
60%+ of analysist time for Idealization (Sandia report)
Recent commercial results
Varity of Midsurface Errors
Process/tools of corrections
Quality Midsurface, a must

## Slide 7: Literature Survey

## Slide 8: Traditional CAD-CAE Transition Approach
Input formats
Elimination of Details - Defeaturing
Dimension Reduction – Medial computation
Validation
Output – Idealized Geometry

## Slide 9: CAD Model Simplification
Feature Recognition-based: Hamdi, Belaziz
Decomposition-based: SH Lee, B Kim
Feature-based: Dabke, Smit

## Slide 10: Midsurface Development Milestones
1967 Blum MAT
1994 Dabke Features for Idealization
1996 Rezayat MA
2007 Robinson Sketch based Midsurface
2013 Woo Decomposition per feature midsurface
2016 Zhu Rib Decomposition

## Slide 11: Medial Axis Transform (MAT)
Blum, Robinson, Ramanathan, etc
Maximal circle/ball, loci of centers
Defined for any input shape
Reversible
Spurious Branches

## Slide 12: Chordal Axis Transform (CAT)
Prasad, Quadros, etc
Constrained Delaunay Triangulation
Any input shape
Missing ends
Does not mimic well

## Slide 13: Thinning
Montanari, Aichholzer, etc.
Offset Inside
Intersection events
Spurious Branches

## Slide 14: Midsurface Abstraction (MA)
Rezayat, S Kim, Sheen
Detect Face Pairs
Midsurface Patches
Extend – Trim
Most representative
Complex, with errors
Commercially adopted

## Slide 15: Feature-based Midsurface
Stolt, Robinson, Boussuge
Single Feature + MAT
Decomposition + Feature Recognition/MA
No feature interaction

## Slide 16: Commercial Midsurface
CAD : Unigraphics NX, Inventor
CAE : Hypermesh, MSc Apex
MA based: Auto + Manual
Quality issues

## Slide 17: Observations from Literature Survey
Most are Brep based and very few leverage feature information
Model Defeaturing
  Selection of features to remove depends on domain, analysis type, etc.
  Most approaches are feature recognition based and size based.
  Feature based deterministic approaches are less, and they still use size criterion
  Size based use full feature dimensions
Midsurface Generation:
  Formal approaches: any shape but need post processing
  Heuristic approaches: More practical, but complexities in Pair detection, Joining
Limited in the range of
  input model geometries (say, only planar or analytic surfaces),
  feature types (say, only extruded, positive primitives) and
  connection types (say, only, parallel, or perpendicular)

## Slide 18: Research Objectives
To develop a system to generate a quality midsurface of feature based CAD model.
To develop defeaturing algorithms to simplify CAD feature model while retaining the gross shape.
To develop algorithms to transform existing sheet metal features to a ﬁnite set of generalized features.
To develop algorithms for generating quality midsurfaces leveraging generalized feature based CAD model and cellular decomposition covering a wide variety of topological connectivities.
To come up with an approach to topologically validate the generated midsurface.
To implement a software system incorporating above algorithms and demonstrate the efﬁcacy of the proposed approach.

## Slide 19: Research Scope
Sheet Metal Parts: 40% Manufacturing parts
Thin-walled Constant Thickness parts
Feature based Autodesk Inventor CAD models

## Slide 20: Proposed System - MidAS
Input: Feature based Autodesk Inventor CAD Model
Each step, a module, OO Interfaces
Model Defeaturing
Feature Generalization
Cellular Decomposition
Midsurface Patch generation (incl Midcurve Computation)
Dormant Features Reapplication
Output: Midsurface

## Slide 21: Model Defeaturing

## Slide 22: Proposed Approach
Need: More features, difficult computation
Objective: Remove irrelevant features, but retain gross shape
Phase I: Sheet Metal Features Taxonomy based
Phase II: Remnant Feature Size based
Phase III: Dormant feature based

## Slide 23: Sheet Metal Features Taxonomy
Sheet metal features classified into categories .
Primary (P) : Principal. Relevant.
Secondary (S): Relevant if > Threshold.
Tertiary/Auxiliary (T): Superficial. Irrelevant.
Feature Groups (G): Collections Relevant if > Threshold.

## Slide 24: Phase I : Defeaturing based on Sheet Metal Feature Taxonomy
Identification based on Taxonomy
Primary features: Cannot be removed as they directly affect the gross shape
Secondary and Group features: Removed if their sizes are below the threshold
Tertiary features: Removed irrespective of their sizes

## Slide 25: Phase II : Defeaturing based on Remnant Feature Size based
Features when booleaned, are consumed
Erroneous if defeaturing decision is based on full feature dimensions
Approach to detect and compute size of the remnant size of features
Size criterion: summation of face areas

## Slide 26: Phase III : Defeaturing based on Dormant features
Large Negative but relevant features
Hindrance to midsurface computation
Tool bodies cached
Re-applied after Midsurface computation

## Slide 27: Effectiveness of Model Defeaturing
Metrics: Percentage reduction in the number of faces.

## Slide 28: Summary: Model Defeaturing
Limitations of existing approaches:
  Feature Recognition unreliable
  Dominance of size based selection
  Wrong size computation
  Loss of negative relevant features
Contributions
  Sheet Metal Features Taxonomy based Approach
  Remnant Feature Approach
  Dormant Feature Approach
  Effective reduction in Features/faces, while retaining the Gross Shape

## Slide 29: Feature Generalization

## Slide 30: Proposed Approach
Need: Presence of a large variety of types of features
Challenging to develop feature based algorithms
Proposed: New CAD representation with Loft as genialized feature form
Objective: To transform given feature tree to generalized feature tree
No loss of ‘feature’-ness
No loss of re-generation

## Slide 31: Proposed New Form Features
ABLE:
  Affine Transformations
  Booleans
  Lofts
  Entities
  CAD model as list of ABLE entities

## Slide 32: Wall - Loft equivalent

## Slide 33: Flange - Loft equivalent

## Slide 34: Transformation to ABLE

## Slide 35
Transformation in ABLE representation

## Slide 36: Summary: Feature Generalization
Limitations of existing approaches:
  Plethora of feature types
  Lack of generic notation for CAD features/entities
Contributions:
  New representation scheme for Feature-based CAD
  Loft as generalized feature form
  Sheet Metal features as Lofts

## Slide 37: Midsurface Generation

## Slide 38: Existing Approach - MA
Limitations
  Face Pairing challenges
  Patch Joining challenges
Proposed Cellular decomposition
Cell classification, delegation

## Slide 39: Interface Configurations

## Slide 40: Feature-based Cellular Decomposition
Features Boolean types are changed from Union to “New”
Concave Edge partitioning in the feature influence zone.
Result:
  non overlapping cells with feature owners
  Face interface between cells
Graph: Cells at nodes and overlapping faces at edges
Classification:
  Solid Cells (Scells)
  Interface Cells (iCells)

## Slide 41: Proposed Approach
Graph to bring connectivity information
Makes overall complexity of original part irrelevant
Rules:
  sCells compute Midsurface patches
  iCells join incident midsurface patches
Delegation of computations
Generic and not type specific rules

## Slide 42: Midsurface Patches in Solid Cells
Two cases
  Offset: profile >> guide : offset the profile face
  Midcurve: profile << guide: compute midcurve, sweep

## Slide 43: Generation of Midcurve
Partition given shape into sub-shapes
Midcurves can be generated for each sub-shape.
Such individual Midcurves are joined

## Slide 44: Polygon Decomposition

## Slide 45: Midcurve Computation

## Slide 46: Results

## Slide 47: Connecting Patches

## Slide 48: Connection Scenarios

## Slide 50: Summary: Midsurface Generation
Limitations of existing approaches:
  Post processing in formal approaches
  Face pair detection and Patch Joining problems
  Manual corrections
Contributions:
  Feature based Cellular Decomposition
  Cellular Graph for connectivity and delegation of computation
  Midcurve generation using enhanced polygon decomposition and cellular midcurve computation
  Midsurface by generic rules

## Slide 51: Re-application of Dormant Features

## Slide 52: Topological Validation

## Slide 53: Validation Types
Manual Inspection for gaps, errors
Tools based inspection: Hausdorﬀ distance.
Recent: Topological Validation: Measures topological entities of the midsurface match with the ones predicted.

## Slide 54: Topological Validation by Lockett

## Slide 55: Approaches for Topological validation
Solid-to-Surface
Find relationship between topological entities of a thin-solid and its corresponding Midsurface.
See if the predicated Midsurface entities validate the non-manifold equation
Surface-to-Solid
Predict the topological entities of possible thin-wall solid that would be source of the given Midsurface.
These predicted entities can be validated against entities of the original thin-solid as well as with the manifold equation

## Slide 56: Solid to Surface

## Slide 57: Surface to Solid

## Slide 58: Results
Solid-Surface: Predict Midsurface entities
Surface-Solid: Predict Solid entities
Contribution:
  New Topological Validation Formulation

## Slide 59: Case studies

## Slide 60: MidAS Implementation
Inventor Professional 2014 – Student edition
Feature based 3D modeller based on ACIS kernel
API support via VB.net

## Slide 61: Benchmarking

## Slide 62: Model Defeaturing

## Slide 63: Feature Generalization

## Slide 64: Cellular Decomposition - Midsurface

## Slide 65: Final Midsurface by Dormant re-application

## Slide 66: Test-case I : Bracket

## Slide 67: Test-case II: Stapler lower bottom

## Slide 68: Test-case III

## Slide 69: Conclusions

## Slide 70: Conclusions
Development of Feature based Midsurface Computation approach
Feature based Defeaturing: Taxonomy, Remnant, Dormant
Feature generalization: Loft as a generic feature
Leveraging Cellular Decomposition for 2D (midcurve), 3D (midsurface) computation
Bi-directional Topological Validation of midsurface
Demonstration of efficacy of the approach in the system implemented, called MidAS

## Slide 71: Research Contributions
Feature-based CAD Algorithm paradigm: Simplification – Generalization – Decomposition – Cellular Graph
Automatic defeaturing of sheet metal feature-based CAD model
  Based on newly developed sheet metal features taxonomy
  Based on newly developed, more accurate criteria of Remnant feature sizes
  Based on newly developed approach of Dormant features
Automatic transformation of sheet metal features to generalized features
  Newly developed generalized CAD model representation, called ABLE
  Transformation mapping of Sheet Metal features to Loft equivalents
Automatic computation of Midsurface
  Midcurve Computation: Enhanced Polygon Decomposition and newly developed cellular midcurve computation
  Midsurface Computation: Cellular graph based, generic logic for connections.
New Topological Validation formulation framework

## Slide 72: Future work
Implementation:
  Internal Development instead of using-API.
  Adopting to different CAD modellers
Domain:
  More sheet metal features
  Catering to Injection moulding domain
Geometric Modelling:
  Development of Feature based Cellular Kernel
  Expansion of ABLE transformations to other fields such as Meshing

## Slide 73: Research Publications
International Journals
  July 2016, Leveraging feature generalization and decomposition to compute a well-connected midsurface, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Engineering with Computers, Springer
  July 2016, Computation of Midsurface by Feature-based Simplification-Abstraction-Decomposition, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Jrnl of Comp and Info Sc in Eng, ASME
  May 2015, Topological Validation of Midsurface Computed from Sheet Metal Part, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Computer-Aided Design and Applications, Taylor & Francis
  June2016, Defeaturing Sheet Metal Part Model based on Feature Information, Yogesh Kulkarni, Ravi Kumar Gupta, Anil Sahasrabudhe, Mukund Kale, Alain Bernard, Computer-Aided Design and Appl, Taylor & Francis
  January 2017, Dimension-Reduction Technique for Polygons, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Intl. Journal of Computer Aided Engineering and Technology}, Inderscience
International Conferences
  June 2015, Defeaturing Sheet Metal Part Model based on Feature Information, Yogesh Kulkarni, Ravi Kumar Gupta, Anil Sahasrabudhe, Mukund Kale, Alain Bernard, Proceedings of CAD 15, London
  December 2014, Formulating Midsurface using Shape Transformations of Form Features, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, 5th Intl. and 26th AIMTDR, IIT Guwahati
  December 2013, Strategies for using feature information in model simplification, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Intl. Conf. on CAE, IIT Madras
  May 2013, Using Features for generation of Midsurface, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Intl. Conf. on Advances in Mech Eng, COEP, India
National Conferences
  January 2014, Midcurves Generation Algorithm for Thin Polygons, Yogesh Kulkarni, Anil Sahasrabudhe, Mukund Kale, Natl. Conf. on Emerging Trends in Eng and Science, Asansol, India.

## Slide 74: Thank you