## Slide 1: Midcurve by Neural Networks
Yogesh Kulkarni

## Slide 2: MidcurveNN : Encoder-Decoder Neural Network for Computing Midcurve of a Thin Polygon

## Slide 3: Introduction

## Slide 4: Strength Analysis by CAE
Aerospace
Machinery
Consumer Products
Industrial equipment
Energy
Construction

## Slide 5: Can we use shapes directly?
CAD : Designing Shapes
CAE : Engineering Analysis
CAD->CAE: Simplification for quicker results.

## Slide 6: CAD-CAE

## Slide 7: For Shapes like Sheet Metal…
 | Solid mesh | Shell+Solid mesh | Difference (%)
Element number | 344,330 | 143,063 | -58%
Node Number | 694,516 | 75,941 | -89%
Total Degrees of freedom | 2,083,548 | 455,646 | -78%
Maximum Von. Mises Stress | 418.4 MPa | 430 MPa | +3%
Meshing + Solving time | Out of memory | 22 mins | N/A (4G RAM)
Meshing + Solving time | 30 mins | 17 mins | -43% (12G RAM)
Half the computation time, but similar accuracy

## Slide 8: Midsurface is?
Input: Solid
Output: Midsurface
Widely used for CAE of Thin-Walled parts
Computation is challenging and still unsolved

## Slide 9: Getting Midsurface
Going on for decades…
Manually by offsetting and stitching, initially
Many CAD-CAE packages give automatic option, but…

## Slide 10: Look at the output

## Slide 11: Can’t tolerate gaps
We have thickness sampling,
To recreate/represent the original shape
Input and output difference not desirable

## Slide 12: For a simple model like

## Slide 13: You get

## Slide 14: For a far simpler shape

## Slide 15: Current Quality
Errors take weeks to correct for complex parts.
But still preferred, due to vast savings time
From Days to hours…

## Slide 16: Midsurface Computation
Midsurface of a Patch is Midcurve of its profile extruded.
So, it boils down to computing 1D midcurve of a 2D profile

## Slide 17: What is a Midcurve?
Midsurface : From 3D thin Solid to 2D Surface
Midcurve : From 2D Profile to 1D Curve

## Slide 18: Many Approaches
More than 6 decades of research…
Most CAD-CAE packages…
Rule-based!! Heuristic!! Case-by-case basis!!

## Slide 19: When-What
1967 Blum MAT
1994 Dabke Features for Idealization
1996 Armstrong MAT for CAE
2002 Deng FBD Simplification
2005 Stolt Pocket Pad Mids
2007 Robinsn Sketch Mids
2012 Russ FBD defeaturing
1999 Fischer Param Midcrv
1996 Rezayat MA SDRC
2013 Woo Decomp, per feature mids

## Slide 20: 2017: My PhD Work: Rule-based

## Slide 21: Limitations
Fully rule-based
Need to adjust for new shapes
So, not scalable

## Slide 22: Idea
Can Neural Networks “learn” the dimension reduction transformation?

## Slide 23: How?
Supply lots of training data of profiles and their corresponding midcurves and train.
Then given an unseen profile, can Neural Network compute a midcurve, mimicking the original profile shape?

## Slide 24: Midcurve by Neural network

## Slide 25: Midcurve : The Problem
Goal: Given a 2D closed shape (closed polygon) find its midcurve (polyline, closed or open)
Input: set of points or set of connected lines, non-intersecting, simple, convex, closed polygon
Output: another set of points or set of connected lines, open/branched polygons possible

## Slide 26: Midcurve == Dimension Reduction
Like PCA (Principal Component Analysis), wish to find Principal curve
That ‘represents’ the original profile shape

## Slide 27: Midcurve == Translation
Left side (input): 2D Sketch Profile
Right Side (output): 1D Midcurve
Sequence 2 Sequence problem

## Slide 28: Midcurve != Auto-Encoder Decoder
Its not Auto-Encoder as Input and Output are different
Its not fixed size i/o as Input and Output sizes are different

## Slide 29: Variable Size Encoder Decoder
Batches need fixed lengths
Made fixed size by Padding.

## Slide 30: Variable Size Encoder Decoder
OK for NLP, say Machine Translations, where padding values like “-1” can be added along with other words (vectors or indices)
But in Geometry, its not OK.
Because any value can represent a Valid Input, even though we don’t want it to be the input.

## Slide 31: A Twist to the problem
Till we get good variable size encoder decoder network for geometry…
Decided to convert this Sequence 2 Sequence problem as Image 2 Image problem.

## Slide 32: A Twist to the problem
Input: Black & White Image of 2D profile
Output: Black & White Image of 1D midcurve

## Slide 33: Solves …
Problems of Geometric sequences
Variable input/output sizes
Loops need to be crossed
Branches

## Slide 34: Reuse Image Encoder Decoder

## Slide 35: For Dimension Reduction

## Slide 36: For Deep Learning
Need lots of data
Had just few input output image pairs
How to augment/populate large variations…

## Slide 37: Data preparation

## Slide 38: Data
Original input and output are in the form of polylines, meaning a list of points, each having x,y coordinates
Profile Data | Profile Picture | Midcurve Data | Midcurve Picture
5.0 5.0 10.0 5.0 10.0 30.0 35.0 30.0 35.0 35.0 5.0 35.0 |  | 7.5 5.0 7.5 32.5 35.0 32.5 7.5 32.5 | 

## Slide 39: Data
For each shape, we have this pair of input and output. That’s it.
We need to start with these few samples only
Profile Data | Profile Picture | Midcurve Data | Midcurve Picture
0 25.0 25.0 25.0 25.0 20.0 15.0 20.0 15.0 0 10.0 0 10.0 20.0 0 20.0 |  | 12.5 0 12.5 22.5 25.0 22.5 0 22.5 | 

## Slide 40: Augmentation
Such few profile shapes, are just not enough for Neural Networks to train.
Need more with as much diversity as possible.
Will need to artificially augment data with transformations, like pan, rotate, mirror, etc.
All needs to be automatically, programmatically

## Slide 41: Geometry to Image
Raw input data is in the Vector format
Converted it to fixed size (100x100) image by rasterization of drawSVG library.

## Slide 42: Variations
Inputs: I, L, Plus, T
Operations:
  Translated
  Rotated
  Mirrored
  Mirrored Translated
  Mirrored Rotated
Total: 896 images (still less, but not bad)

## Slide 43: Training Data Samples

## Slide 44: Midcurve By neural network

## Slide 45: Options For Architectures
Simple Encoder Decoder (one layer each)
Dense Encoder Decoder
Convolutional Encoder Decoder
Pix2Pix
…

## Slide 46: Simple Encoder Decoder

## Slide 47: Simple Encoder Decoder

## Slide 48: Keras Implementation
input_img = Input(shape=(input_dim,))
encoded = Dense(encoding_dim, activation='relu',activity_regularizer=regularizers.l1(10e-5))(input_img)
decoded = Dense(input_dim, activation='sigmoid')(encoded)
autoencoder = Model(input_img, decoded)
encoder = Model(input_img, encoded)
encoded_input = Input(shape=(encoding_dim,))
decoder_layer = autoencoder.layers[-1]
decoder = Model(encoded_input, decoder_layer(encoded_input))
autoencoder.compile(optimizer='adadelta', loss='binary_crossentropy')

## Slide 49: Results

## Slide 50: Results
Not very perfect but encouraging
NN is correct with
  The location (bounding box)
  Dimension Reduction is seen
But, still some stray points and misses

## Slide 51: What can be done?
For the noise, use bounding boxes
Feedback into error term: differencing with the known output expected
Classify single pixel image as the skeleton, and rest as noise.

## Slide 52: What Next?
Add denoiser network after the current one
More Network Architectures
Sequence-to-Sequence based approaches, taking closed thin polygon as input and polyline as output
Extending to 3D, ie Midsurface

## Slide 53: End notes

## Slide 54: Summary
Various applications need lower dimensional representation of shapes.
Midcurve is one- dimensional(1D) representation of a two-dimensional (2D) planar shape.
Used in animation, shape matching, retrieval, finite element analysis, etc.

## Slide 55: Summary
Approaches: Thinning, Medial Axis Transform (MAT), Chordal Axis Transform (CAT), Straight Skeletons, etc., all of which are rule-based.
Proposing a novel method called MidcurveNN which uses Encoder-Decoder neural network for computing midcurve from images of 2D thin polygons in supervised learning manner.

## Slide 56: Summary
This dimension reduction transformation from input 2D thin polygon image to output 1D midcurve image is learnt by the neural network,
Which can then be used to compute midcurve of an unseen 2D thin polygonal shape.

## Slide 57
Thank you
yogeshkulkarni@yahoo.com